## Slide 1: EagleEye: Wearable Camera-based Person Identification in Crowded Urban Spaces
Juheon Yi1, Sunghyun Choi2, Youngki Lee1
1Seoul National University, 2Samsung Research Korea
ACM MobiCom 2020

## Slide 2: Needs for Robust Person Identification
Finding a crime suspect in crowded streets
Children counting in kindergarten field trips

## Slide 3: Humans: How Fast and Accurate?
Difficult due to large number of faces and their small sizes

## Slide 4: User Study Results
Humans are vulnerable to cognitive overload
25 participants (age 24-32), 15 images per participant
Crowdedness level: low/medium/high
Latency increases to 16 seconds
Accuracy drops to 75%

## Slide 5: EagleEye: AR Person Identification System

## Slide 6: Key Challenges
How to accurately recognize small faces captured from distance?
How to run multi-DNN face identification in real-time on mobile?

## Slide 7: Challenge #1: Identification Accuracy
Lack of resolution blurs the decision boundaries
112x112
56x56
28x28
14x14

## Slide 8: Apply Image Super-Resolution?
GANs reconstruct realistic faces, but do not preserve the identity
Existing approaches: heavily Generative Adversarial Network (GAN)-based
Ground truth
LR face
GAN

## Slide 9: Identity Clarification Network (ICN)
Generator ()
Landmark-aided HR face reconstruction
Enforce reconstructed face to preserve facial features
Enforce reconstructed face to look realistic

## Slide 10: Observation for Improvements
Face feature distance for varying resolutions
Same identity pair
Different identity pair
When resolution is low, True Positive drops significantly

## Slide 11: Identity-Specific Fine Tuning
Observation: we know who we are looking for
Reference photos
Downsampled
Update weights
Reconstructed
Pre-trained ICN
ICN training loss
Utilize reference photos to overfit towards the target

## Slide 12: Challenge #2: Computational Complexity
[1] J. Deng et al., “RetinaFace: Single-stage Dense Face Localisation in the wild,” arXiv 2019.
[2] J. Deng et al., “ArcFace: Additive Angular Margin Loss for Deep Face Recognition,” CVPR 2019.
Sequential on-device execution takes 14 seconds to process a scene with 30 faces
648 ms per 1080p frame [1]
166 ms per 14x14 face
287 ms per 112x112 face [2]
* measured on LG V50 (Qualcomm Adreno 640 GPU) with TensorFlow-Lite

## Slide 13: Content-Adaptive Parallel Execution
Spatial Pipelining processes regions in parallel over mobile and cloud
Edge-Based Background Filtering removes background regions from processing
Variation-Adaptive Face Recognition
selects pipeline based on difficulty

## Slide 14: Content-Adaptive Parallel Execution
Variation-Adaptive Face Recognition
selects pipeline based on difficulty
Spatial Pipelining processes regions in parallel over mobile and cloud
Edge-Based Background Filtering removes background regions from processing

## Slide 15: Edge-Based Background Filtering
Edge filtering saves 64% of computation with 2 ms overhead
Edges give a hint on where faces would be
Notes: So the first step is edge-based background filtering.
The goal here is to rule out the background regions in the image to avoid unnecessary computation.
The tricky part here is that we need to do it without actually running the face detection. This is, but we have found that the edges in a scene gives a loose hint on where the faces would be
So give a scene …
Of course this edge-based filtering is not perfect, as we cannot rule out the regions with dense non-face objects like the tree, and it may actually fail on a scene full of objects. However, even in such cases, the latency of running the edge detector is typically very small and the cost will be negligible.

## Slide 16: Content-Adaptive Parallel Execution
Spatial Pipelining processes regions in parallel over mobile and cloud
Edge-Based Background Filtering removes background regions from processing
Variation-Adaptive Face Recognition
selects pipeline based on difficulty

## Slide 17: Variation-Adaptive Face Recognition
Recognition difficulty heavily depends on face variations
Easy
Hard
Model | Inference time | LFW (easy faces)
MobileFaceNet | 14 ms | 98.9%
ArcFace | 287 ms | 99.3%
overkill!

## Slide 18: Variation-Adaptive Face Recognition
Is the resolution sufficient?
Is the pose frontal?
No
Yes
No
Yes
ICN + ArcFace
ArcFace
MobileFaceNet

## Slide 19: Content-Adaptive Parallel Execution
Variation-Adaptive Face Recognition
selects pipeline based on difficulty
Spatial Pipelining processes regions in parallel over mobile and cloud
Edge-Based Background Filtering removes background regions from processing

## Slide 20: Execution Planning
DNNs to execute
RetinaFace
ICN
ArcFace
MobileFaceNet
① Background  Excluded
② Large, frontal faces  RetinaFace + MobileFaceNet
③ Large, profile faces
 RetinaFace + ArcFace
④ Small faces
 RetinaFace + ICN + ArcFace
Available processors
Mobile CPU
Mobile GPU
Cloud GPU
?

## Slide 21: Execution Planning
High-resolution image
Large GPU memory I/O latency
High network bandwidth consumption

## Slide 22: Execution Planning
High-resolution image
Mobile CPU

## Slide 23: Execution Planning
High-resolution image
Mobile CPU
Proportional to the number of faces
166/287 ms per face on mobile GPU
6/7 ms per face on cloud GPU

## Slide 24: Execution Planning
High-resolution image
Mobile CPU
Proportional to the number of faces
Local GPU: MobileFaceNet (18 ms)
Cloud GPU: ICN + ArcFace (6 + 7 ms)

## Slide 25: Spatial Pipelining
Time
①
②
③
Mobile CPU
D
on ①
D
on ②
D
on ③
Mobile GPU
L
L
L
L
L
L
L
L
L
L
Cloud GPU
I +H
H
I +H
I +H
I +H
I +H
H
I +H
I +H
D
Detection
L
Lightweight
recognition
H
Heavy
recognition
I+H
ICN + Heavy
recognition
②
②
③
③
①
①

## Slide 26: EagleEye: Putting Things Together
Divide and process in units of image blocks
Filter background blocks
Run face detection on scene
Run face recognition on detected faces

## Slide 27: Evaluation
How much accuracy improvement does EagleEye achieve?
How much latency improvement does EagleEye achieve?
How effectively does EagleEye utilize mobile and cloud resources?

## Slide 28: Low-Resolution Face Recognition Accuracy
ICN enhances True Positive by 78% at the cost of 14% False Positive
ICN training dataset: Flickr-Faces-HQ (FFHQ)
Test dataset: VGGFace2
112x112
14x14
Fine-tuned
Baseline

## Slide 29: Latency on Crowded Scenes
Latency gain increases with crowdedness (as high as 9.07x)
Tested device: LG V50 (Adreno 640 GPU)
Tested LTE bandwidth: 11 Mbps
(A: Adaptive recognition, P: Spatial pipelining, E: Edge-based background filtering)
Result on a high scene with 20 faces (hard/easy faces mixed)
9.07x
Low
Medium
High
4.1s
5.9s
8.5s
1.0s
0.9s
0.9s
8.6s
6.5s
1.3s
0.9s

## Slide 30: Comparison with Alternatives
Latency/accuracy on High scenes
EagleEye outperforms both full on-device and offloading with only 108 KBytes offloaded
End-to-end latency
Top-K accuracy
5.7s
8.5s
3.4s
0.6s
0.9s

## Slide 31: Rooms for Improvements
Utilizing the temporal redundancy of videos
Dynamic DNN-processor mapping depending on scene contents
User interface design to utilize EagleEye as a full AR service

## Slide 32: Summary
We present EagleEye, an AR-based person identification system on mobile devices
  ICN enhances LR face recognition accuracy (78% gain in TP at the cost of 14% FP)
  Content-Adaptive Parallel Execution enhances face identification latency by 9.07x
For more questions, contact Juheon Yi at johnyi0606@snu.ac.kr
Juheon Yi, Sunghyun Choi, and Youngki Lee, “EagleEye: Wearable camera-based person identification in crowded urban spaces”