## Slide 1: BlueScan: Boosting Wi-Fi Scanning Efficiency Using Bluetooth Radio
Juheon Yi, Weiping Sun, Jonghoe Koo,
Seongho Byeon, Jaehyuk Choi, and Sunghyun Choi
June 13th, 2018

## Slide 2: Introduction
Proliferation of IEEE 802.11 WLAN (Wi-Fi)
Limited coverage of Wi-Fi Access Points (APs)
  Stations need to frequently search for neighboring APs (Wi-Fi scanning)
Inevitable inefficiency: no prior knowledge about neighboring APs
  Stations need to search for APs on every Wi-Fi channel
   Unnecessary energy consumption & delay
Can we make it “smoother” without requiring additional hardware?
Introduction ●
?
AP 1
AP 2

## Slide 3: Motivation
Our approach
  Employ Bluetooth radio to detect neighboring APs prior to Wi-Fi scanning
Why Bluetooth?
  Low power
  Widely available in smartphones (as Wi-Fi & Bluetooth combo chipset)
Is it worth it?
  40% of Wi-Fi devices still remain 2.4 GHz only
  Most dual band devices connect to 2.4 GHz Wi-Fi networks
Preliminaries ●○
Low power
Combo chipset

## Slide 4: BlueScan: Overview
Design philosophy
  Bluetooth radio tells “when” and “where” to search for neighboring APs
How can Bluetooth radio detect Wi-Fi APs?
  Periodic beacon frames transmitted at Target Beacon Transmission Time (TBTT)
   98.6% of Wi-Fi APs employ fixed 102.4 beacon period
Overall flow of BlueScan
Preliminaries ○●
Covered whole 2.4 GHz?
Yes
No
Enhanced Wi-Fi scanning
AP channel pinpointing
Beacon frame detection
Choose RSSI sampling channel
Bluetooth
Wi-Fi
Operating channels
& TBTTs of APs

## Slide 5: Beacon Frame Detection (1/2)
What makes it difficult?
  CSMA/CA distorts the periodicity
  Beacon frames are scarce (one in every 102.4 )
Goal
  Desired output: number of APs in the channel & corresponding TBTTs
  Adapt RSSI sampling time depending on channel utilization
Our algorithm in essence
  ① Find beacon frame candidates from RSSI samples
  ② Check for periodicity among candidates (in aware of CSMA/CA)
  ③ If periodicity is strong, declare them as beacon frames
  ④ If there is a vague periodicity, sample more RSSI until things become clear
Proposed Scheme ●○○○

## Slide 6: Beacon Frame Detection (2/2)
Our algorithm in details
  ① Extract segments and classify depending on idle time before segment start
  ② Search for periodicity among segments depending on type
  ③ How do we determine whether to stop of continue RSSI sampling?
    Depending on classification using credibility
  ④ If any vague set exists, sample RSSI for additional 102.4 and repeat ①-③
Proposed Scheme ○●○○
Time
TBTT detected!
Type-1 segment
Beacon period
Type-2 segment
RSSI samples
2
1
2
1
2
1
2
1
C = 3/3  beacon frame!
C = 2/3  vague!
Notes: ④⑤

## Slide 7: AP Channel Pinpointing
Beacon frames can be observed on neighboring channels
However, they will be congruent with respect to modulo 102.4 ()
Naïve approach
  Detect beacon frames on every channel & group congruent ones
   May incur a long delay
Proposed Scheme ○○●○

## Slide 8: AP Channel Pinpointing
Beacon frames can be observed on neighboring channels
However, they will be congruent with respect to modulo 102.4 ()
Naïve approach
  Detect beacon frames on every channel & group congruent ones
   May incur a long delay
Proposed Scheme ○○●○
TBTT%102.4
AP at channel 3
2
4
6
8
10
12
False positive
Beacon detected
1
3
5
7
9
11
Channel
13
AP at channel 6
AP at channel 9

## Slide 9: AP Channel Pinpointing
Beacon frames can be observed on neighboring channels
However, they will be congruent with respect to modulo 102.4 ()
Naïve approach
  Detect beacon frames on every channel & group congruent ones
Enhanced solution: detect-and-verify process
  Detect on even numbered channels & verify on neighboring channels
Proposed Scheme ○○●○
TBTT%102.4
AP at channel 3
2
4
6
8
10
12
Ambiguous
Ambiguous
Ambiguous
Beacon detected
1
3
5
7
9
11
Channel
13

## Slide 10: AP Channel Pinpointing
?
?
?
?
Beacon frames can be observed on neighboring channels
However, they will be congruent with respect to modulo 102.4 ()
Naïve approach
  Detect beacon frames on every channel & group congruent ones
Enhanced solution: detect-and-verify process
  Detect on even numbered channels & verify on neighboring channels
Proposed Scheme ○○●○
TBTT%102.4
AP at channel 3
2
4
6
8
10
12
False positive
Beacon detected
1
3
5
7
9
11
Channel
13

Beacon verified
AP at channel 6
AP at channel 9
?
?
?
?
?




## Slide 11: Enhanced Wi-Fi Scanning
Now we know the channels & TBTTs of neighboring APs
We can choose “when” and “where” to trigger Wi-Fi scanning!
Two options to boost Wi-Fi scanning efficiency
  ① Selective active scanning
    Trigger active scanning only on channels where APs are present
     Enhanced delay efficiency
  ② Scheduled passive scanning
    Wake up at the TBTT to listen for beacon frame
     Enhanced energy efficiency
Proposed Scheme ○○○●

## Slide 12: Prototype Implementation
Prototype implementation on laptop
  Bluetooth radio: Ubertooth-one
  Wi-Fi: ath9k (AR9380)
  Python subprocess module to manage interaction
Currently, system parameters are determined empirically
Evaluation ●○○○

## Slide 13: Performance of Beacon Frame Detection
Comparison scheme
  ZiFi[1] (ZigBee based Wi-Fi AP detector)
Detection accuracy
  Single AP scenario
    BlueScan achieves both high TP and low FP
  Multiple APs scenario
    Accuracy invariant to the number of APs
Detection delay
  Adaptive to channel utilization
  Lower delay compared to ZiFi
[1] R. Zhou et al, “ZiFi: Wireless LAN Discovery via ZigBee Interference Signatures ,” in Proc. ACM MobiCom 2010.
Evaluation ○●○○

## Slide 14: Performance of AP Channel Pinpointing
Channel pinpointing delay
  3 APs on channel 2, 7, 13
  Detect-and-verify process achieves 54% shorter delay
Channel pinpointing accuracy
  2 APs on channel 6, 7
  Detect-and-verify process causes slight imbalance depending on channel
Evaluation ○○●○

## Slide 15: Scanning Delay & Energy Consumption
Scanning delay measurement
  Baseline
    Active scanning
    (scan time = 40 per channel)
  Delay reduction
    Selective active: 77%
    Scheduled passive: 53%
    (Rx time: 88%)
Energy consumption modeling
  Little overhead once Bluetooth detects neighboring APs
Evaluation ○○○●

## Slide 16: Summary
Proposed Bluetooth aided Wi-Fi scanning scheme
  Periodic beacon frame & TBTT detection
  AP channel pinpointing
  Enhanced Wi-Fi scanning (selective active, scheduled passive scanning)
Performance enhancement
  Up to 77% Wi-Fi scanning delay reduction
Future work
  Parameter optimization
  Evaluation for handoff
Conclusion ●

## Slide 17
Thank you for your attention
!

## Slide 18: Real World Experiment
Residential environment
  4 APs at channel 4, 6, 7, 13
TBTT acquisition accuracy
  Ground truth TBTT is estimated using Tcpdump
  BlueScan accurately detects the TBTTs of APs
    TBTT acquisition error < 300 μs (mainly due to USB transfer delay)
Backup Slides